## Slide 1: ODC functional chain views

## Slide 2: Mission
One Driving Core
Our joint mission:
  Using different sensor sets we shall find the best possible “ADAS control behavior”. Then using different actuator sets will shall execute the “ADAS control behavior” in the best possible way.
ADAS Control Behavior is not exactly the same as todays SIT-BS behavior.
Notes: -

## Slide 3: ADAS Control Framework for Driving Vision
© Robert Bosch GmbH 2016. Alle Rechte vorbehalten, auch bzgl. jeder Verfügung, Verwertung, Reproduktion, Bearbeitung, Weitergabe sowie für den Fall von Schutzrechtsanmeldungen.
8
ADAS Control Framework is the Bosch Operating System for all future Driver Assistance Systems including HAD. It runs customer specific Apps on various Sensor- and Computing Platforms, abstracting from E/E architecture and includes mainstream reference implementations.
Common
Domain Model
One System
Architecture*
One ADAS
Framework
Compatible with
One BBM
System Architecture
* Based on common work and test model and artefacts to product lines, test runs for complete ADAS control framework to avoid braking changes by isolated SW changes
Situation Reaction
Analysis Pattern
Perception
Motion Planning and Control
Acting
Environment Sensing
Computing and
Communication
Resources
Behaviour
...
Highway
Pilot
Lane Keeping
Support
Adapt. Cruise Control
Parking Pilot
Vehicle Environment
Actuators / External Sensors / HMI / C2X IF
Sensor
Radar
Sensor
Video
Sensor
Ultra-sonic
Domain Computer
DASy
Brake System
Powertrain System
Steering System
Sensor
VMS-x
Target values/ Feedback
ADAS Control System ADAS Control Framework*
Behaviour
Perception
Interpretation
Sensing
Ego Motion Planning
Reaction
Actuating
Motion Control & Actuator Mmgt.

## Slide 4: Functional chain
FCT
© Robert Bosch GmbH 2018. All rights reserved, also regarding any disposal, exploitation, reproduction, editing, distribution, as well as in the event of applications for industrial property rights.
2
One Driving Core
Problem break-down along functional chain:
Perception
Motion Control & Actuator Mmgt.
Sensorset 1
BC-Env.-Mod.
Behaviour and system
evaluation
Behaviour and Trajectory
Planning
Actuatorset 1
Sensorset 2
Actuatorset 2
Decision on behaviour
Ego vehicle Mod.
Ego Motion Generation
Driver Mod.
Aggregate/Collect all measured information about the environment, the driver and the ego vehicle
Check plausibility of information also by adding a priori knowledge
Plan different behaviors and trajectories – possibly with different level of detail
Evaluate all planned behaviors and provide metrics. Evaluate system uncertainty.
Decide on a behavior based on the provided metrics
Prepare behavior and Target Path and Trajectory for execution
Provides kinematic target state for vehicle
Provide actor target values to reach target motion based on vehicle kinetic response
Notes: Vielleicht cut an der Stelle wo mehr Informationen von VMC in den nächsten Schritt einfließen als von DACore?

## Slide 5
PT
STR
Brake
Intern | Chassis Systems Control | Dr. Markus Voss (CC-DA/EYD5) | 18.04.2016
Plausibilized
Environment Model
Behaviors
Behavior
Strategy
Agents
SIT
ODC One Driving Core
PER
Common
Environment Model
Sensor-specific Object Hypothesizes
ENS-L
ENS-M
Host Vehicle
Behavior Simulation
Behavior Execution
RPM
ACC
FCT (APP)
AEB
AEB-VRU
TJA
HWA
TJP
HWP
ENS-V
ENS-R
Behavior Evaluation
Safe and Feasible Situation Filters
ENS-N
DSM
DDM
CCD
SVB (APP)
Service Level Coordination
Diagnostic Information
Mgmt.
Computing
Communication
System Time
Math
Persistent Data
Dispatching
DiaTester
CCR-Radar
CCR-Video
CCR-DASy
CCR-Radar
CCR-Radar
CCR-US
CCR-NRCS
Ego Motion Planner
Motion Control & Actuator Mgmt.
MCAM
EGM
EMS
Ego Motion and State Estimation

## Slide 6: Functional chain
One Driving Core
Sensor characteristics
Radar: Locations (dx, dy, dv, dΦ)
Video: Lines, Textures, …
Estimated status of environment model
Moving objects: dx, dy, dv, quality
Road border construction: dx, dy, geometry, quality
Driving lane: number of lanes, topology, curve radius, quality
Ego Motion and State Estimation
Static: Weight, dimensions, …
Dynamic: Velocity, yaw rate, steering angle, track, …
Driver model
Presence, attention, viewing direction, tiredness level, …
Trajectory Corridor
Reaktion pattern selection & parametrization
Estimated behaviour strategy wrt intention
- Comfortable driving
Fast moving forward
Accident free driving
Accident severity minimization
confrom to regulations
Economic driving
Driver intention
Plausible estimated status of environment model
EGM (Ego Motion Generation)
MCAM (Motion Control and Actuator Management)
Actuator Control
Set point values
Target powertrain / brake force
Target Steering angle
Actuator Feedback
Pedal position
Actual powertrain / brake force
Motion Target Values:
- Lat Target yaw rate, curvature
- Long Target ax, jerk limits
subsystem
subsystem

## Slide 7: E&E cuts / interfaces to actuators within ODC scope
One Driving Core
Brake System
ADAS ECUs
ADAS Control System ODC: One Driving Core
Sensor
Ultra-sonic
Sensor
Video
Sensor
Radar
Domain Computer
DASy
Steering System
Str angle
Str trq
- Fx
-ax
+/-ax
Trajectory
Trajectory +/-ax +/-Fx
Str angle Str trq
+/-ax +/- Fx
-ax - Fx
- Fx
Powertrain System
ax
ax Fx
Fx
Fx
FCT
Str trq
Sign Sensors
Lane Sensors
Obstacle Sensors
Map Sensors
Lbs Sensors