## Slide 1: Adaptive cruise control (ACC) Modular kit
Customer communication material
Released Version: October 2021 – All displayed information subject to change

## Slide 2: The longitudinal control in SAE Level 1 & 2
The Adaptive cruise control extends the standard cruise control with an automatic adjustment of the speed and distance to the preceding vehicle.
deceleration
Adaptive cruise control
distance
acceleration

## Slide 3: …Bosch driving assist - modular kit
Adaptive cruise control is part of the…
Level 1
Level 2

## Slide 4: Features & Value-add features  Portfolio  Roadmap  Upgrades over time

## Slide 5: Main features in series production
Adaptive cruise control portfolio
Adaptive cruise control
base
In series
In series
  Speed range: 30 kph – 250 kph (maximum speed depending on sensor set)
  Distance to preceding vehicle can be adjusted by driver
  Comfortable speed adaptations inside curves (standard value-add feature: Curve speed controller)
  Speed range: 0 kph – 250 kph (max. speed depending on sensor set)
  Automatic resume within 3s after ego vehicle stand still
  Starts the engine when direct preceding vehicle is driving off
  Optional value-add feature: Braking on standing objects available
  Implicit and explicit speed signs are recognized (with feature: Road sign information)
  Predictive and comfortable speed adaptations before curves (optional value-add available for more complex use cases, like intersections)
  Automatic or confirmed adaptation modes supported
Adaptive cruise control
stop & go
Adaptive cruise control
plus
In series
In series
Note: Minimum & maximum speed and functional performance depending on sensor set and selected ACC feature

## Slide 6: Value-add features – Overview (1/2)
Adaptive cruise control
Personalized drive programs
Different acceleration and deceleration characteristics
Optional: consumption optimized measures
s
s
s
Curve speed controller
Reduction of ego vehicle speed based on lateral acceleration
Cooperative behavior
Situation based gap generation to support lane change of neighboring vehicle
Speed adaptation based on driver lane change request and traffic in neighboring lane
o
o
o
Wrong side overtake avoidance
Speed reduction to avoid illegal overtaking on the wrong side
Applies to traffic rules of specific countries
o
o
Predictive overtaking support
Foresees the driver intention to change the lane due to an overtaking scenario
Assists the driver by avoiding unnecessary decelerations due to the preceding vehicle
o
o
o
ACC engine start base
Engine starts when preceding vehicle drives-off or when the driver resumes ACC
s
s
Overtaking support
Speed increase of ego vehicle if driver intends to overtake
Verification against preceding or overtaking vehicles on the neighboring lane
o
o
o
s: standard equipped
o: optional
Adaptive cruise control
stop & go
plus
base
s
s
s
o
*Concept phase, timing and content not finalized yet

## Slide 7: Value-add features – Overview (2/2)
Adaptive cruise control
ACC engine start plus
Adaptive distance control
Right of way support
Braking on standing objects
ACC reaction on standing object (vehicles)
Brings ego vehicle to standstill; Maximum speed of ego vehicle depending on sensor set
Automatic resume plus
Re-activates the ACC feature after the ego vehicle came to a complete stop within ACC control and the preceding vehicle drives off
ACC resumes automatically within 30s after ego vehicle standstill
o
o
Eco drive mode*
Implementation of energy-efficient speed optimization integrated in ADAS architecture
  Initiates the start of the engine when the pre-preceding vehicle drives off
  Feature can additionally be active in ACC passive mode
Warning and reaction to stop/yield signs and red traffic lights
Brings vehicle to a complete stop at red traffic lights
s
o
o
o
When driving not in ACC mode the Adaptive distance control ensures a comfortable distance to the preceding vehicle and takes over braking maneuvers
o
o
Adaptive cruise control
Adaptation to road radius
Ego vehicle speed is adapted automatically to road radius
Curve radius, intersection, roundabout radius and traffic behavior information are considered
s
o
o
s: standard equipped
o: optional
Adaptation to road hazards*
Considers cloud-based environmental information to adapt safety distance and driving speed to the actual driving condition pro-actively before the vehicle is encountering any dangerous situation
s
o
stop & go
plus
*Concept phase, timing and content not finalized yet

## Slide 8: Value-add feature Roadmap
Adaptive cruise control
Note: Value-add feature description and versioning attached as one-pager in the chapter “Value-add feature description”

## Slide 9: Upgrades over time
Adaptive cruise control
… production software updates or
… over the air vehicle software updates
… and diverse business models like:
  traditional running change model
  regular maintenance model
Features can be upgraded over time to production vehicles or field vehicles using…

## Slide 10: Feature description

## Slide 11: Adaptive cruise control base
Feature description
PRID0041
Feature description
The Adaptive cruise control base extends the standard cruise control with an automatic adjustment of the speed and distance to the preceding vehicle.
  Speed range: 30 kph – 250 kph (maximum speed depending on sensor set)
  Distance to preceding vehicle can be adjusted by driver
  Comfortable speed adaptations inside curves (Value-add feature: Curve speed controller)
Customer benefits
  Increase in driving comfort: relieve from adjusting speed and safety distance to current traffic situation
  Natural comfort braking when approaching a preceding, slower vehicle
Increase in safety: reduces speed already before any Automatic emergency braking (AEB) feature is triggered
For OEMs: different scalable technology solutions available
Required technology elements
    Diverse sensor solutions available:
      (1) Standard & recommended: Front Radar and Front Video
      (2) Front video only (with performance limitations)
      (3) Front Radar only (with performance limitations)

## Slide 12: Adaptive cruise control stop & go
Feature description
PRID0007
Feature description
The Adaptive cruise control stop & go extends the standard ACC base with an automatic adjustment of the speed and distance to the preceding vehicle in stop & go traffic situations.
  Speed range: 0 kph – 250 kph (max. speed depending on sensor set)
  Automatic resume within 3s after ego vehicle stand still
  Starts the engine when direct preceding vehicle is driving off
  Optional sub feature: Braking on standing objects available
Customer benefits
  Increase in driving comfort: relieve from adjusting speed and safety distance to current traffic situation even in stop & go situations
  feature can be used within the complete speed range
For OEMs: different scalable technology solutions available
Required technology elements
    Diverse sensor solutions available:
      (1) Standard & recommended: Front Radar and Front Video
      (2) Front video only (with performance limitations)
      (3) Front Radar only (with performance limitations)
    Automatic transmission
    Support of standstill management based on braking system (e.g. Automatic parking brake)

## Slide 13: Adaptive cruise control plus
Feature description
PRID0005
Feature description
The Adaptive cruise control plus extends the ACC stop & go with a predictive, automatic speed adjustment according to the actual speed limit and to characteristics of the road radius.
  Implicit and explicit speed signs are recognized (with feature: Road sign information)
  Predictive and comfortable speed adaptations before curves (optional value-add available for more complex use cases, like intersections)
  Automatic or confirmed adaptation modes supported
Customer benefits
Increased comfort: less driver interaction required, more natural driving style
Supports Euro NCAP: points for (1) automatic ACC set speed adaptation or (2) offer to the driver to change manually the set speed
Increase in safety: speed limits are always followed and over speeding in curves is avoided
Required technology elements
    Diverse sensor solutions available:
      (1) Standard & recommended: Front Radar and Front Video
      (2) Front video (with performance limitations)
    Feature: Road sign information
    Map with curve radius and road sign attributes

## Slide 14: Value-add feature description

## Slide 15: Curve speed controller
Value-add feature description
lateral acceleration
Feature description
The Curve speed controller controls the lateral acceleration by reducing the ego vehicle speed inside curves.
The allowed maximum lateral acceleration can be adjusted vehicle individually according to OEM requirements
A speed dependency can be applied to the allowed maximum lateral acceleration
The maximum allowed lateral acceleration can be adjusted for different driving modes of the vehicle
Customer benefits
  Keeps target speed in case of loss of target object in curves
  Increases safety and comfort in curves if ACC target speed setting is too high (avoids the need to cancel ACC)
For OEMs: cost efficient solution without additional technology elements
Required technology elements (additional to main feature)
ACC plus
ACC base
ACC stop & go
Standard
Standard
Standard
PRID0272
    No additional technology element necessary
    Optional: Roundabout information to optimize controller inside roundabouts:
        Unplausible acceleration inside the roundabout will be suppressed
        At the exit of the roundabout the acceleration is improved to avoid unnatural decelerations of the ego vehicle.

## Slide 16: Personalized drive programs
Value-add feature description
Feature description
The Personalized drive programs adapts the ACC dynamic behavior using predefined settings
The dynamic behavior can be adjusted by OEM in each program and can be combined with other drive programs (e.g. from engine management)
Several drive programs are supported
Regional specific applications are supported
Customer benefits
  Increased end user experience: “my personal ACC”
  Completes personalized drive programs from engine, steering and others
  Supports also consumption optimization modes like for example Eco modes
Required technology elements (additional to main feature)
    HMI concept and signal interface to provide information about selected drive program
ACC plus
ACC base
ACC stop & go
Standard
Standard
Standard
PRID0273
Sport+
Individual
Dynamic
Auto
Efficiency
Sport
Comfort
Eco

## Slide 17: Cooperative behavior
ACC plus
ACC base
ACC stop & go
Optional
Optional
Optional
Value-add feature description
Feature description
The Cooperative behavior reacts to neighboring vehicles both (1) when the driver indicates a lane change or (2) when a neighboring vehicle intends a lane change to the ego lane due to a slower preceding vehicle.
(1) Speed reduction to position ego vehicle at a gap of the neighboring vehicles to allow lane change of ego vehicle
(2) Gap to preceding vehicle is increased to allow neighboring vehicle a lane change into ego lane
Customer benefits
  Improves overall traffic flow by considering neighboring lane vehicles and their behavior
  Increases the natural driving behavior of the main feature
  Reduced driver interactions
Required technology elements (additional to main feature)
    No additional technology element necessary
PRID0280
(1)
(2)
>

## Slide 18: Wrong side overtaking avoidance
Value-add feature description
Feature description
The Wrong side overtaking avoidance prevents an unwanted overtaking at the ‘wrong’ side while ACC is active.
Ego vehicle keeps distance to preceding vehicle in the neighboring lane
Related traffic rule applies to some target countries
Customer benefits
  Prevents the driver to cancel ACC in case of a wrong side overtaking scenario
  Supports driver to increases safety while ACC is active
Required technology elements (additional to main feature)
    Geofencing if required for specific target country and road selection (according to the state specific legal conditions)
PRID0203
ACC plus
ACC base
ACC stop & go
Optional
Optional
Optional

## Slide 19: Overtaking support
ACC plus
ACC base
ACC stop & go
Optional
Optional
Optional
Value-add feature description
Feature description
The Overtake support increases speed of ego vehicle if driver intends to overtake (driver triggered by turn indicator)
If driver does not perform overtaking maneuver, speed and distance will again be adapted to preceding vehicle
An increase of the ego speed is verified against preceding or overtaking vehicles on the neighboring lane
Customer benefits
  Less interaction of driver needed
  Natural driving behavior on multiple lane roads while overtaking
  Supports natural traffic flow
Required technology elements (additional to main feature)
    Recommended: Rear corner radar for blind spot scenarios
PRID0215
Speed increase
80kph
80kph
Set-speed: 130kph

## Slide 20: Predictive overtaking support
Value-add feature description
ACC plus
ACC base
ACC stop & go
Optional
Optional
Optional
Feature description
The Predictive overtaking support foresees the driver intention to change the lane due to an overtaking scenario (free neighboring lane and slower preceding vehicle). It assists the driver by avoiding unnecessary decelerations due to the preceding vehicle.
Ego vehicle speed is kept longer, and deceleration is delayed due to the slower preceding vehicle
If driver is not starting the lane change, higher deceleration is applied to keep safety distance
Customer benefits
  Less interaction of driver needed
  Keeps ego vehicle target speed in standard lane change use cases
  Natural driving behavior on multiple lane roads while overtaking
Required technology elements (additional to main feature)
    Rear corner radar for blind spot scenarios
PRID0274
Predicted driver intention
120kph
80kph

## Slide 21: Eco drive mode*
Value-add feature description
Feature description
Eco drive mode is a comprehensive, pre-integrated Bosch solution to make ADAS features drive more energy-efficiently
Eco drive mode is activated by the driver
Energy efficient driving using road geometry and topology information (based on map data and environment perception)
Implementation of energy-efficient speed optimization integrated in AD / ADAS architecture in cooperation with the powertrain and engine management
Customer benefits
  Increase energy-efficiency of ADAS (~5%** for EVs)
  Solution integrated within ADAS features yields the best system optimum of powertrain and assisted features
For consumers: increased vehicle driving range, reduced energy cost, more relaxed driving
For OEMs: increase vehicle driving range or decrease battery size, green image, not relevant to OBD regulations
Required technology elements (additional to main feature)
Make ADAS features drive more energy-efficiently
*Concept phase, timing and content not finalized yet
PRID0202
ACC plus
ACC base
ACC stop & go
Not available
Optional
Not available
    Optional: Map with road gradient information
** based on in-house simulation

## Slide 22: ACC engine start base
Value-add feature description
ACC plus
ACC base
ACC stop & go
Standard
Standard
Not available
Feature description
The ACC engine start base initiates the start of the engine when the direct preceding vehicle drives off.
The start of the engine is only initiated after the ego vehicle came to a complete stop behind a preceding vehicle and the engine was turned off by the Start/Stop system.
The feature is only starting the ego vehicles engine, no drive-off
Customer benefits
  Prepares a drive-off scenarios by decreasing the reaction time
  Reminds the driver using feedback from the engine start to resume ACC (in case a manual ACC resume is necessary)
Required technology elements (additional to main feature)
    No additional technology element necessary
PRID0212

## Slide 23: ACC engine start plus
Value-add feature description
Feature description
The ACC engine start plus adds additional features to the base version:
  Initiates the start of the engine when the pre-preceding vehicle drives off
  Feature can be active in ACC passive mode
Customer benefits
  Very early preparation in drive-off scenarios by decreasing the reaction time
  With the support of ACC passive mode this sub feature can always be offered to the driver
  Reminds the driver using feedback from the engine start to resume ACC (in case a manual ACC resume is necessary)
Required technology elements (additional to main feature)
    No additional technology element necessary
PRID0291
ACC plus
ACC base
ACC stop & go
Optional
Optional
Not available

## Slide 24: Braking on standing objects
Value-add feature description
ACC plus
ACC base
ACC stop & go
Optional
Standard
Not available
Feature description
PRID0213
Required technology elements (additional to main feature)
Customer benefits
  Increases safety by reducing the ego vehicle speed before AEB features are triggered
  No interaction of driver needed when approaching a standing vehicle
Ego vehicle max speed: 60kph
Ego vehicle max speed: 80kph
Ego vehicle max speed: 130kph
The Reaction on standing objects decelerates comfortably to standing vehicles in the ego lane.
Feature is active below an ego vehicle speed of:
V1: 60kph
V2: 80kph
V3*: 130kph
      Front video mandatory
      V3*: Localization on road level
*Concept phase, timing and content not finalized yet

## Slide 25: Automatic resume plus
Value-add feature description
ACC plus
ACC base
ACC stop & go
Optional
Optional
Not available
Feature description
ACC stop & go and ACC plus include an automatic drive-off after the preceding vehicle moves off. The Auto-resume time window is extended to 30s (V1) or unlimited (V2).
V1: Automatic resume plus active within 30s after ego vehicle standstill
V2*: Automatic resume plus active without any time limitations
Required technology elements (additional to main feature)
For V1: Front Radar, Intruder detection support (by e.g., Front camera, Near range cameras or Ultra sonic sensors); Optional: Driver monitoring camera with driver attentiveness detection
    For V2*: In concept phase
Customer benefits
  The driver does not need to resume the ACC feature manually
  Less interaction of driver needed
  Increased comfort in dense traffic scenarios
PRID0275
30 seconds
No time limitation
30
∞
*Concept phase, timing and content not finalized yet

## Slide 26: Right of way support
Value-add feature description
Feature description
Customer benefits
  Extends the availability of ACC to stop/yield signs, traffic lights and more
  Supports driver to increase safety while ACC is active
Required technology elements (additional to main feature)
V1/V2: Localization on road level (e.g. Road signature base); Behavior and hazard map (Map base)
V3 / V4*: Localization on lane level (e.g. Road signature enhanced); XD map (Map enhanced)
ACC plus
ACC base
ACC stop & go
Not available
Optional
Not available
Warnings and speed reductions
Warnings
Complete stop or speed reduction
Complete stop*
The Right of way control reacts to stop/yield signs and red traffic lights while ACC is activated. The feature is upgraded constantly over time.
V1: while approaching a stop or a yield sign a warning is displayed and the ego vehicle speed is reduced to support the warning to the driver
V2: while approaching a red traffic light the driver is warned and the ego vehicle speed is reduced to support the warning to the driver
V3: ego vehicle comes to a complete stop at a stop sign or at a yield sign the ego speed is reduced accordingly; At other infrastructure elements like bumpers or crosswalks the ego vehicle speed is reduced accordingly
V4*: at a red traffic light the ego vehicle comes to a complete stop
PRID0282
*Concept phase, timing and content not finalized yet

## Slide 27: Adaptation to road radius
Value-add feature description
Feature description
The Road topology adaptation feature adjusts the ACC vehicle speed to the road geometry in a predictive manner.
V1: speed adaptation to curve radius including round abouts
V2: speed adaptation at intersections or any other lane splits using navigation route information and/or vehicle indicator
V3: Additional usage of traffic behavior speed information (swarm data) to adjust speed for curves and turns.
Customer benefits
  Increases safety and comfort in curves if ACC target speed setting is too high for the given road geometry
  Avoids the need to cancel ACC in curves
Keeps target speed in case of loss of target object in curves
Required technology elements (additional to main feature)
ACC plus
ACC base
ACC stop & go
Not available
Standard
Not available
Speed adaptation to curve radius
Speed adaptation based on traffic behavior information
Speed adaptation following navigation route or vehicle indicator
PRID0281
    V2: Map with radius information of intersections
    V3: - Bosch connected map service (behavior layer)
    - Connected horizon
    - Mobile communication unit

## Slide 28: Adaptation to road hazards*
Value-add feature description
PRID0076
Feature description
The Road hazard adaptation feature considers cloud-based environmental information to adapt safety distance and driving speed to the actual driving condition pro-actively before the vehicle is encountering a supported hazardous situation, e.g:
Road surface condition: slippery road
Road hazards: obstacle, accident, breakdown or wrong way driver vehicle
Visibility hazards: fog, smoke or heavy rain/snow
V1: confirmation of adaptation by driver (SOP Q2/2022)
V2: automatic adaptation without driver confirmation (SOP Q1/2024)
Customer benefits
Increase of safety and comfort in a pro-active and predictive way for drivers using ACC
Increased natural driving behavior
After 2023/25, road hazards will most likely be NCAP and IIHS relevant
Required technology elements (additional to main feature)
    Bosch connected map service (road hazard layer)
    Connected horizon
    Mobile communication unit
ACC plus
ACC base
ACC Stop & Go
Optional
Standard
Not available
*Concept phase, timing and content not finalized yet

## Slide 29: Adaptive distance control
Value-add feature description
ACC plus
ACC base
ACC stop & go
Optional
Optional
Not available
Feature description
When driving yourself the Adaptive distance control ensures a comfortable distance to the preceding vehicle and takes over braking maneuvers.
The ego vehicle supports the driver in keeping a safe distance to the preceding vehicle by actively reducing the acceleration and controlling the deceleration
The distance to the preceding vehicle can be changed continuously by the driver using the accelerator pedal
Once activated, the feature is not deactivated by a brake application
The feature can be manually disengaged by the driver
Customer benefits
  Closes the gap between ACC and AEB features
  Increased safety due to an early and comfortable distance control before AEB features are triggered
  Increased comfort for the driver: easy one pedal drive
  In dense traffic situations: less driver adaptions of the accelerator pedal necessary
  Very natural and intuitive driving experience
  Usage of existing ACC hardware (including HMI)
Required technology elements (additional to main feature)
    Front Radar
PRID0071